## Slide 1: Radio Frequency Readout Device (RFRD) Phase - II
Fall 2017

## Slide 2: Group 11
Advisors
  Dr. Daji Qiao
  Dr. Nathan Neihart
Graduate Students
  Scott Melvin
  Chengrui Yang
Students
  Bailey Akers
  Colin Sunderman
  Nathan Mulbrook
  Lyle Bishop
  Pengyu Qu

## Slide 3: Problem Statement
Purpose:
  To reduce the time it takes to check tightness of nut on anchor bolts
  Each nut is torqued manually to check tightness
Solution:
  Create an Radio Frequency Readout Device (RFRD)
  Passively powered from the RF reader
  Measures tightness of the nut by measuring the capacitance of two washers
    As nut loosens, capacitance decreases
  Washer has tag attached

## Slide 4: Functional Requirements
Wireless operation
Passively powered tag
Measure capacitance of washers
Send data back to reader
Operating environment
  Not addressed in this design

## Slide 5: Non-Functional Requirements
Conforms to FCC Regulations
  ISM (902-928MHz)
Size
  Components have potential to be scaled down in future revisions
Reasonable cost

## Slide 6: Market Survey
RFRD Readers and Tags
  Implemented in market products
Measuring bolt tightness using RFRD
  Implemented in certain research applications
Our application is unique in measuring bolt tightness
  By measuring capacitance of the washers

## Slide 7: System Block Diagram
Notes: Slide before add subteams

## Slide 8: Design Groups
Capacitance Measuring
  Bailey Akers and Colin Sunderman
Antenna and Power Harvesting
  Lyle Bishop and Pengyu Qu
RFRD Communication Protocol / Microcontroller
  Nathan Mulbrook

## Slide 9: Capacitance Measurement Functional Requirements
Operate with low power
  Antenna team research
  Approximately 0.45mW expected
Measure capacitance from 20pF to 50pF
  LCR measurements performed on washer
Notes: Slide before add subteams

## Slide 10: Relaxation Oscillator
Creates a PWM signal
Period is dependent on capacitance

## Slide 11: Relaxation Oscillator
VTH = Vout/2, if Ra = Rb and Vref = 0
Vi > VTH, then Vout = VL-
Vi < VTH, then Vout = VL+
VTH

## Slide 12: Comparator – TS881
Manufacturer: STMicroelectronics
Low power comparator
  Supply voltage 0.85 V to 5.5 V
  220 nA typical supply current
    No load, output high
  Operates at approximately 1 uW
    Assuming +/- 1.8 V supply
  SPICE model

## Slide 13: Simulation
Calculated Period:
T = 55us for C = 50pF
T = 33us for C = 30pF

## Slide 14: C = 50pF
Simulated: T = 53us
Calculated: T = 55us

## Slide 15: C = 30pF
Simulated: T = 35us
Calculated: T = 33us

## Slide 16: Conclusion
The relaxation oscillator allows us to calculate the capacitance
Can use Ra and Rb to control the voltage the capacitor charges to
Can use R and C to control the period of the pulse widths

## Slide 17: Capacitance Measurement Test Plan
Prototype the design on breadboard
Test for different values of capacitances and resistors and verify that results are consistent
  Tune the oscillation frequency
  Balance power, microcontroller design, and quality of measurement
Find the amount of power consumed

## Slide 18: Antenna Design
Inverted F antenna
  More compact
  Microstrip format
  900MHz
Estimated power from similar applications
  Fractal loop antenna

## Slide 19: Antenna Design

## Slide 20: Antenna Test Plan
Simulating antenna design in ADS
Creating rectifier in PSpice

## Slide 21: Future Plans
Antenna simulation
  Tune antenna to 900 MHz
Need to simulate rectifier
  PSPICE
Couple rectifier to antenna
  ADS
Possible backscatter implementation

## Slide 22: RFRD Communications Design
Radio Transmitter
  Send power to the tag
SDR
  Receives data from tag
GNU Radio
  Process received signal

## Slide 23: RFRD Communications Requirements
Unique Identifiers for Tag
Transmission integrity
  Checksum
Microcontroller
  Low power

## Slide 24: Project Status
Capacitance Measuring
  Simulated design with TS88
  Ordered TS881
  Breadboard prototype
Antenna
  DN023 Inverted-F design
  Simulating using ADS software
RFRD Communication Protocol
  Plan for implementation

## Slide 25
Notes: Move to future plans slide. Highlight current progress.

## Slide 26: Future Plans
Capacitance Measuring:
  Build circuit and test
Antenna Design:
  Simulate antenna
  Design and simulate a rectifier
Communications Design:
  Implement receiver in GNU Radio
  Write software for microcontroller
Notes: Add Gantt chart afterwards

## Slide 27: References
Liu, Yili, et al. “Limitations of a relaxation oscillator in capacitance measurements.” IEEE Transactions on Instrumentation and Measurement, vol. 49, no. 5, 2000, pp. 980–983., doi:10.1109/19.872917.
Tuttle, Dr. Gary. “Non Linear Oscillators.” EE 230 Website, Dr. Gary Tuttle, tuttle.merc.iastate.edu/ee230/topics/op_amps/non_linear_oscillators.pdf.
“TS881 Rail-To-Rail 0.9 V nanopower comparator.” www.st.com/content/ccc/resource/technical/document/datasheet/a2/60/3e/5d/b2/c1/4a/e9/DM00057901.pdf/files/DM00057901.pdf/jcr:content/translations/en.DM00057901.pdf.
Zeng, Miaowang, et al. “A Compact Fractal Loop Rectenna for RF Energy Harvesting.” IEEE Antennas and Wireless Propagation Letters, vol. 16, 2017, pp. 2424–2427., doi:10.1109/lawp.2017.2722460.
Kervel, Fredirk. “868 MHz, 915 MHz and 955 MHz Inverted F Antenna.” www.ti.com/lit/an/swra228c/swra228c.pdf.