## Slide 1: Radio Frequency Readout Device (RFRD)
Spring 2018

## Slide 2: Group 11
Advisors/Clients
  Dr. Daji Qiao
  Dr. Nathan Neihart
Graduate Students
  Scott Melvin
  Chengrui Yang
Students
  Bailey Akers
  Colin Sunderman
  Nathan Mulbrook
  Pengyu Qu

## Slide 3: Problem Statement
Purpose:
  Reduce field time while manually checking nut tightness on anchor bolts

## Slide 4: Problem Statement
Solution:
  Create an Radio Frequency Readout Device (RFRD)
  Passively powered
  Measures tightness of the nut by measuring the capacitance of two washers
    As nut loosens, capacitance decreases
  Indicate whether the nut is tight or loose to signal servicing

## Slide 5: System Block Diagram
Notes: Slide before add subteams

## Slide 6: Functional Requirements
Wireless operation
  Passively powered
Measure capacitance of washer design
Visual indication of nut tightness
Operating environment
  Not addressed in this design
  Indoor conditions

## Slide 7: Non-Functional Requirements
Conforms to FCC Regulations
  ISM frequencies
Size
  Components have potential to be scaled down in future revisions
Reasonable cost
Relevant standard
  1720-2012-IEEE Recommended Practice for Near-Field Antenna Measurements

## Slide 8: Design Groups
Antenna and Rectifier
  Pengyu Qu
Capacitance Measuring
  Bailey Akers and Colin Sunderman
Microcontroller
  Nathan Mulbrook

## Slide 9: Antenna/Rectifier Design
Inverted F antenna
  Compact in size
  Microstrip format
  Central operating frequency: ~950 MHz
  Can be operated at ISM frequencies (~915 MHz)
Rectifier
  2V/100uW output minimum
  Simulated at 915 MHz

## Slide 10: Antenna Design

## Slide 11: Antenna Test Results
Central frequency: 950 MHz

## Slide 12: Rectifier Design

## Slide 13: Rectifier Test Results
Simulations at 0 dBm input:
Output voltage: 2.404 V
Output power: 115.6 uW
Power Conversion Efficiency (PCE): 0.116

## Slide 14: Antenna/Rectifier PCB layout

## Slide 15: Capacitance Measurement Functional Requirements
Operate with low power
  - Rectifier supplies up to
  115.6 uW
Measure capacitance from 20pF to 600pF
Measure capacitance of washer design
  - 20 pF resting washers
  - 30-40 pF pressured washers
Notes: Slide before add subteams

## Slide 16: Relaxation Oscillator
VTH = Vout/2, if Ra = Rb and Vref = 0
Vi > VTH, then Vout = VL-
Vi < VTH, then Vout = VL+

## Slide 17: Capacitance Measuring / Microcontroller PCB
Outputs pulse wave
Low power (44.5 uW measured)
Designed with test and isolation points
Vcc+ = 2V, Vcc- = 0V, COM = 1V

## Slide 18: Capacitance Measuring / Microcontroller PCB Testing
  Period linearly dependent on capacitance measured

## Slide 19: Capacitance Measuring / Microcontroller PCB Testing
  Acceptable power supply rejection ratio

## Slide 20: Microcontroller Design
Microcontroller
  STM32L011K4 low power ARM
  Nucleo development board
  Small package size
Measure signal from capacitance measuring circuit
Turn LED on at threshold period
  Corresponds to nut tightness
  Demonstrated with threshold of 30 pF

## Slide 21: Toolchain
System Workbench for STM32
  Eclipse
CubeMX
  Peripheral initialization
  Clock initialization

## Slide 22: Signal Measurement
Threshold frequency calculated at compile
Uses low power timer as a counter
  Triggers on rising edge
Counts for 1000ms
Measured frequency is compared to threshold and GPIO outputs are set

## Slide 23: Testing and Verification
UART and debugging was not available for testing of final firmware version
Test various threshold values and ensure operation
Test current draw to ensure proper low power operation

## Slide 24: System Testing Setup
Microcontroller
Tx Antenna
Capacitance Measuring PCB
Rx Antenna
Rectifier
Washers

## Slide 25: System Testing Results
Resting Washer

## Slide 26: System Testing Results
Pressured Washer

## Slide 27: System Testing Results
Demonstrated wireless operation at 3.25 inches from Tx to Rx antenna
Signal generator supplied 15.5 dBm at 887 MHz to the Tx antenna
  To guarantee 2 volts DC supplied to PCB
Microcontroller and capacitance measuring circuit fully operational
Successfully operated with washer design
  Triggered LED when pressured

## Slide 28: End of Project Results
Capacitance Measuring:
  Functional design and PCB
  Low power operation
Antenna/Rectifier Design:
  Simulated antenna/rectifier
  Modeled PCB design
Microcontroller Design:
  Functional firmware and PCB
  System Design:
  Successful demonstration of wireless functionality
  Measured washer design with capacitance measuring circuit
  Triggered LED with microcontroller threshold
Notes: Add Gantt chart afterwards

## Slide 29: Future Revisions
Capacitance Measuring:
  Scalability of the PCB
Antenna/Rectifier Design:
  Fabricate the PCB
  Test the PCB
  Implement backscatter
Microcontroller Design:
  Persistent tag ID and data tracking
  Implement protocol
  Communication to RF reader
Notes: Add Gantt chart afterwards

## Slide 30: References
Liu, Yili, et al. “Limitations of a relaxation oscillator in capacitance measurements.” IEEE Transactions on Instrumentation and Measurement, vol. 49, no. 5, 2000, pp. 980–983., doi:10.1109/19.872917.
Tuttle, Dr. Gary. “Non Linear Oscillators.” EE 230 Website, Dr. Gary Tuttle, tuttle.merc.iastate.edu/ee230/topics/op_amps/non_linear_oscillators.pdf.
“TS881 Rail-To-Rail 0.9 V nanopower comparator.” www.st.com/content/ccc/resource/technical/document/datasheet/a2/60/3e/5d/b2/c1/4a/e9/DM00057901.pdf/files/DM00057901.pdf/jcr:content/translations/en.DM00057901.pdf.
Zeng, Miaowang, et al. “A Compact Fractal Loop Rectenna for RF Energy Harvesting.” IEEE Antennas and Wireless Propagation Letters, vol. 16, 2017, pp. 2424–2427., doi:10.1109/lawp.2017.2722460.
Kervel, Fredirk. “868 MHz, 915 MHz and 955 MHz Inverted F Antenna.” www.ti.com/lit/an/swra228c/swra228c.pdf.
Technologies, Avago. “Linear Models forDiode Surface Mount Packages.”www.avagotech.com, 21 July 2010, ddd.uab.cat/pub/trerecpro/2010/hdl.../PFC_SergiCarreraColet_annex.pdf.
STMicroelectronics. “Access Line Ultra-Low-Power 32-Bit MCU Arm®-Based Cortex®-M0 , up to 16KB Flash, 2KB SRAM, 512B EEPROM, ADC.”www.st.com/resource/en/datasheet/stm32l011d4.pdf.
STMicroelectronics. “STM32 Nucleo-32 board.”http://www.st.com/resource/en/data_brief/nucleo-f031k6.pdf.

## Slide 32: Clocks

## Slide 33: Peripherals

## Slide 34: Final Code
#define THRESHOLD_PERIOD 857
#define THRESHOLD_FREQUENCY (1000000/THRESHOLD_PERIOD)
uint16_t first_cap = 0;
uint16_t last_cap = 0;
while (1){
first_cap = HAL_LPTIM_ReadCounter(&hlptim1); //read initial timer count
HAL_Delay(1000); //wait while number of cycles is counted
last_cap = HAL_LPTIM_ReadCounter(&hlptim1); //read second count value
uint16_t cycles = last_cap - first_cap; //calculate cycles during period
if (last_cap < first_cap){ //handle overflow of counter
cycles = (last_cap + 0xFFFF) - first_cap;
}
if (cycles > (THRESHOLD_FREQUENCY )){ //if the washer is not pressed
HAL_GPIO_WritePin(GPIOB, GPIO_PIN_3, GPIO_PIN_RESET); //LED off
} else {
HAL_GPIO_WritePin(GPIOB, GPIO_PIN_3, GPIO_PIN_SET); //LED on
}
}